## Slide 1: EDS CSV Extraction Guide
Joseph Kern
January 8th, 2020
Email: jkern34@gatech.edu

## Slide 2: 1. Open Pathfinder

## Slide 3: 2. Choose your folder

## Slide 4: 3. Choose Spectral Imaging. If you haven’t taken the EDS Scan yet do so as normal. Otherwise choose the old EDS reading you want.

## Slide 5: 4. Once you have your reading (new or old), choose map processing, and change to Quant. Change “Map Data Type” to “Atomic %”, “output resolution” to “high detail”, “processing accuracy” to “high precision”, and “kernel size” to “1x1”. Process. For Weight % the procedure is the same, just switch “Map Data Type” to Weight %.

## Slide 6: 5. Process your scan from counts to Atomic%

## Slide 7: 6. Make sure you have all the element readings you need. You can left click an element and hover over “quant lines” to ensure the K or L lines are checked

## Slide 8: 7. Export the image to CSV: Go to “file”, “import/export” and choose “export image as CSV”

## Slide 9: 8. Choose your CSV save folder. The file name you choose will have the format: filename_element K/L

## Slide 10: 9. Ensure the grey image is saved in CSV format as well. This will be entitled filename_Grey. If it is there skip to step 13

## Slide 11: 10. If the Grey image CSV is not saved, then click a random old file and then reload the EDS mapping you care about (see step 11)

## Slide 12: 11. Random file

## Slide 13: 12. File you care about. With just the image open (do not click process) go to “export image as CSV” again and save it as your filename (not filename_Grey)

## Slide 14: Contacts for questions
Joseph Kern
  email: jkern34@wisc.edu